## Slide 1
SYED HASAN SAEED
Email: hasansaeedcontrol@gmail.com
Web Page: hasansaeed872726549.wordpress.com
Shasansaeed.yolasite.com

## Slide 2: OUTLINE
Introduction to Analogous System.
Force-Voltage Analogy.
Force-Current Analogy.
Example on Analogous System.
Mechanical Equivalent Network.

## Slide 3: BOOKS
AUTOMATIC CONTROL SYSTEM: KUO & GOLANARAGHI
2. CONTROL SYSTEM: ANAND KUMAR
3. AUTOMATIC CONTROL SYSTEM: S. HASAN SAEED
ELECTRICAL MACINE & AUTOMATIC CONTROL: J.B.GUPTA & S. HASAN SAEED
AUTOMATIC CONTROL SYSTEM: R. A . BARAPATE

## Slide 4: ANALOGOUS SYSTEM
Apply KVL in Series RLC Circuit
aaanna

## Slide 5
Consider parallel RLC circuit and apply KCL
I

## Slide 6: We know the equation of mechanical system
Compare equation(5) with equation(2)
FORCE –VOLTAGE ANALOGY (f-v)
S.NO. | TRANSLATIONAL SYSTEM | ELECTRICAL SYSTEM
1. | Force (F) | Voltage (E)
2. | Mass (M) | Inductance (L)
3. | Stiffness (K), Elastance (1/K) | Reciprocal of C, Capacitance (C)
4. | Damping coefficient (B) | Resistance (R)
5. | Displacement (x) | Charge (q)

## Slide 7: Compare equation (5) with equation (4)
FORCE-CURRENT ANALOGY
S.NO. | TRANSLATIONAL SYSTEM | ELECTRICAL SYSTEM
1. | Force (F) | Current (I)
2. | Mass (M) | Capacitance (C)
3. | Damping coefficient (B) | Reciprocal of resistance (1/R) i.e conductance (G)
4. | Stiffness (K), Elastance (1/K) | Reciprocal of inductance (1/L)
5. | Displacement (x) | Flux linkage (φ)
6. | Velocity | Voltage (E)

## Slide 8: For rotational system
Torque-voltage (T-V) analogy
Compare equation(2) with equation (6)
S.NO. | ROTATIONAL SYSTEM | ELECTRICAL SYSTEM
1. | Torque (T) | Voltage (E)
2. | Moment of inertia (J) | Inductance (L)
3. | Damping coefficient (B) | Resistance (R)
4. | Stiffness (K), Elastance (1/K) | Reciprocal of capacitance (1/C). Capacitance (C)
5. | Angular displacement (θ) | Charge (q)
6. | Angular velocity (ω) | Current (I)

## Slide 9: Compare equation (4) with equation (6)
TORQUE(T)-CURRENT (I) ANALOGY
S.NO. | ROTATIONAL SYSTEM | ELECTRICAL SYSTEM
1. | Torque (T) | Current (I)
2. | Moment of inertia (J) | Capacitance (C)
3. | Damping coefficient (B) | Reciprocal of resistance (R), conductance (G)
4. | Stiffness (K), Elastance (1/K) | Reciprocal of inductance (1/L)
5. | Angular displacement (ω) | Flux linkage (φ)

## Slide 10: Draw the analogous electrical network of the given fig. using f-v analogy
V

## Slide 11: MECHANICAL EQUIVALENT NETWORK
PROCEDURE TO DRAW THE MECHANICAL EQUVALENT NETWORK:
Step 1: Draw a reference line.
Step 2: Corresponding to the displacement x1 x2 ….select the nodes.
Step 3: Connect one end of masses to the reference line
Step 4: Connect other elements of the system to the nodes.
Step 5: Apply nodal analysis, write the system equations.

## Slide 12: Example: (i) Draw the mechanical network of the given system (ii) Draw the analogous electrical system use f-i analogous(assume wheels are frictionless).

## Slide 13
Analogous Circuit (f-I analogy)
1/R1 (B1)
1/L2 (K2)
C2
(M2)
C1
(M1)
1/L1
(K1)
i(t)
f(t)

## Slide 14
f-v analogy
V
L2
L1
R1
R3
R2
1/C1
1/C2
q1
q2

## Slide 15
THANK YOU FOR YOUR ATTENTION