## Slide 1: SYSTEM & AUTOMATIC CONTROL EC217 CONCEPT OF POLES AND ZEROS
SYED HASAN SAEED
Declaration : The content of the presentation has been created for academic use / non-commercial use with fair dealing.

## Slide 2
AUTOMATIC CONTROL SYSTEMS
BOOKS
CONTROL SYSTEM B.C. KUO
CONTROL SYSTEMS K. OGATTA
CONTROL SYSTEMS NAGRATH & KOTHARI
AUTOMATIC CONTROL SYSTEMS S.HASAN SAEED
AUTOMATIC CONTROL SYSTEMS R. A. BARAPATE
CONTROL SYSTEM A. ANAND KUMAR

## Slide 3: OUTLINE
Definition of Transfer Function.
Poles & Zeros.
Characteristic Equation.
Advantages and Disadvantages of Transfer Function.
Transfer Function of given Electrical Network.
Transfer Function from given differential equation and vice - versa
Pole – Zero Plot from given transfer function.

## Slide 4
TRANSFER FUNCTION: Transfer function of any physical system is that mathematical function from which we can determine the complete dynamic behavior of the system. Transfer function can be defined as
“ For any linear, time invariant system, the ratio of Laplace transform of the output to the Laplace transform of input with all initial conditions are assumed to zero.” is known as transfer function.
Consider the block diagram of a system as shown in fig
SYSTEM
Reference input r (t)
Controlled
Output c (t)
G (s)
R (s)
C (s)
Transfer Function =
ℒ Output
ℒ Input
Initial conditions = 0
CONCEPT OF POLES AND ZEROS

## Slide 5: CONCEPT OF POLES AND ZEROS
Let C(s) is the polynomial of order mth and R(s) is the polynomial of nth
Then transfer function can be represented as
CHARACTERISTIC EQUATION: The characteristic equation can be obtained by equating the denominator polynomial of the transfer function to zero. That is

## Slide 6: CONCEPT OF POLES AND ZEROS
Consider the equation (1) in factored form as
POLES : The poles of G (s) are those values of ‘s’ which make G(s) tend to infinity. Where ‘s’ is a special frequency.
ZEROS: The zeros of G (s) are those values of ‘s’ which make G(s) tend to zero.

## Slide 7: CONCEPT OF POLES AND ZEROS
If either poles or zeros coincide, then such type of poles or zeros are called multiple poles or zeros, otherwise they are known as simple poles or zeros.
z1, z2, z3, ….. and p1, p2, p3, …….. are called complex frequencies.
The zeros of the network function tell us what values of ‘s’ will make the function zero, and the poles of a network function tell us what values of ‘s’ will make the function infinite. At other frequency , the network function has a finite non-zero value. For this reason, the poles and zeros collectively are called critical frequencies or critical values of the network function.
The poles and zeros are also known as the roots of the network function.

## Slide 8: CONCEPT OF POLES AND ZEROS
Example (1) consider the following transfer function of a system
This transfer function having the simple poles at s = 0, s = - 2, multiple poles at s = - 4 and simple zero at s = - 3, Gain factor (K) is 50.
ORDER AND TYPE OF THE SYSTEM:
Number of the poles at the origin gives the type of the system. Example (1) is type ‘ 1’ system because one pole is at origin.
Highest power of ‘s’ in denominator of transfer function is called the order of the system. The denominator of example (1) is of order 4, the given system is of order 4.

## Slide 9
CONCEPT OF POLES AND ZEROS
Advantages of Transfer Function:
Transfer function is a mathematical model of all system components and hence of the overall system and therefore it gives the gain of the system.
Since Laplace transform is used, it converts time domain equations to simple algebraic equations.
With the help of transfer function, poles, zeros and characteristic equation can be determine.
The differential equation of the system can be obtained by replacing ‘s’ with d/dt.
Disadvantages of Transfer Function:
Transfer function cannot be defined for non-linear system.
From the Transfer function , physical structure of a system cannot determine.
Initial conditions loose their importance.

## Slide 10: CONCEPT OF POLES AND ZEROS Find the transfer function of the given figure.
Solution:
Step 1: Apply KVL in mesh 1 and mesh 2

## Slide 11
Step 2: take Laplace transform of eq. (1) and (2)
Step 3: calculation of transfer function
Equation (5) is the required transfer function
CONCEPT OF POLES AND ZEROS

## Slide 12
A system having input x(t) and output y(t) is represented by
Equation (1). Find the transfer function of the system.
Solution: taking Laplace transform of equation (1)
G(s) is the required transfer function
CONCEPT OF POLES AND ZEROS

## Slide 13
The transfer function of the given system is given by
Find the differential equation of the system having input x(t) and output y(t).
Solution:
Taking inverse Laplace transform, we have
Required differential equation is
CONCEPT OF POLES AND ZEROS

## Slide 14
Example 1: Plot the pole-zero of the following transfer function.
Im
Re
0
- 1
- 2
- 3
- 4
Poles are represented by and zeros are represented as
S - plane
j1
j2
j3
- j1
- j2
CONCEPT OF POLES AND ZEROS

## Slide 15
Example 2: Plot the pole-zero of the following transfer function.
CONCEPT OF POLES AND ZEROS
SOLUTION:
Im
Re
-1
-2
-3
0
-1
1
-2
S- plane
K = 50
- 2 + j 1
- 2 - j 1

## Slide 16
CONCEPT OF POLES AND ZEROS
EXAMPLE 3: Find the critical frequencies for
and draw the pole-zero plot.
SOLUTION:
-1
-2
-3
-4
-5
j1
j2
j3
j4
j5
- j1
- j2
- j3
0
Im
Re
(2)
The number in parenthesis indicates no. of zeros

## Slide 17
THANK YOU
shasansaeed@yolasite.com
hasansaeed872726549.wordpress.com
saeed.moodlecloud.com
syedhasansaeed.gnomio.com