## Slide 1: CIRCUIT THEORY BASIC TERMS AND DEFINITION

## Slide 2
SYED HASAN SAEED
Email
hasansaeedcontrol@gmail.com
URL
http://shasansaeed.yolasite.com/
http://hasansaeed872726549.wordpress.com/
http://syedhasansaeed.gnomio.com/
Declaration: The content of the presentation has been created for academic use /non-commercial use with fair dealing.

## Slide 3
REFERENCE BOOKS
Introductory Circuit Analysis, Robert L. Boylested, Pearson Education, Prentice Hall.
Networks And Systems, Ashfaq Husain, Khanna Book Publishing Co (P) Ltd. Delhi.
Networks And Systems, A Sudhakar, Shyammohan S Palli, Tata McGraw Hill, New Delhi.
Network Analysis, M.E. Van Valkenburg, PHI Learning Private limited, New Delhi.
Circuit Analysis Principle and Applications, Allan H. Robbins &Wilhelm C. Miller, DELMAR CENGAGE Learning, Indian Reprint.
Network Analysis and Synthesis, Pankaj Swarnkar, Satya Parkashan, New Delhi.

## Slide 4: BASIC TERMS AND DEFINITIONS
NETWORK: Network is an arrangement of different network elements (passive or active) connected in any manner, so that the energy can be transferred from the point of supply to the point of load.
CIRCUIT: Circuit is the network, which must have at least one closed path, so that current can flow in it. So all circuits are network but all networks are not circuit.
NETWORK ANALYSIS: It is the process to find the output or response, when the network and input are known.
NETWORK SYNTHESIS: It is the process to design the network, when the reference input and the desired output are known.

## Slide 5: BASIC TERMS AND DEFINITIONS
CURRENT: Electric current is defined as the time rate of net motion of electric charge in any conductor. Unit is Ampere (A)
POTENTIAL: Potential is defined as the work done to transfer unit positive charge from infinity to any point in electric field. Its unit is volt. It is also known as voltage.
POTENTIAL DIFFERENCE: It is given by work required to transfer unit positive charge from one point to the other. Electrical energy flows from higher potential to lower potential.
POWER: Power is defined as the rate of change of energy.
p = v * I and energy is given by

## Slide 6: BASIC TERMS AND DEFINITIONS
POWER IN AC CIRCUIT: Power in ac circuit is classified as
Apparent Power:
Product of voltage and current. Its unit is volt-amp.
S = VI Volt-Amp = I2 Z where Z is the impedance in ohms
Active Power:
It is given by P = VI cosθ Watt
Active Power also given by P = I2 R
Reactive Power:
It is power taken by the reactance and its unit is volt-amp-reactive (Var). It is given by Q = V I sinθ Var = I2X
Where ‘X’ is the reactance in ohms
P
S
Q
θ
Power Triangle

## Slide 7: BASIC TERMS AND DEFINITIONS
NETWORK ELEMENTS:
Active Elements: These are energy suppliers in electrical network. Active elements may be classified as (i) Voltage source (ii) Current source.
These sources may be independent sources and dependent sources.
Independent Voltage Source: It is the two terminal device. The voltage across these two terminals remain constant irrespective of all circuit conditions.
Symbol:
+
V
+
V
+
V(t)
V(t) =
Vm sinωt or, Vm cosωt
Direct Source
Alternating Source
-
-
-

## Slide 8: BASIC TERMS AND DEFINITIONS
Ideal voltage source: Independent voltage source, which has zero internal resistance is considered as the ideal source. The V-I characteristic shown in fig
Practical voltage source: Source having some amount of internal resistance is known as the Practical source. Due to this resistance, voltage drop takes place and it causes the terminal voltage to reduce.
v
V-I characteristic of practical voltage source
i
0
V-I characteristic of ideal voltage source
i
v
V
0

## Slide 9: BASIC TERMS AND DEFINITIONS
Independent current source: It is also two terminal device, and gives the constant current, irrespective the external circuit condition.
Ideal Current Source: Ideal current source has the infinite resistance. The symbol and V-I characteristic is shown in fig.
I or i(t)
v
0
V-I characteristic of ideal current source
ideal current source
i

## Slide 10: BASIC TERMS AND DEFINITIONS
Practical current source: It has the internal resistance R (in Mega ohms). The symbol and V-I characteristic are shown in fig.
v
0
V-I characteristic of practical current source
I or i(t)
R
Source Symbol
i

## Slide 11: BASIC TERMS AND DEFINITIONS
DEPENDENT OR CONTROLLED ENERGY SOURCE
Voltage Controlled Voltage Source (VCVS):
Here the voltage across source terminal Vab is dependent upon the Vcd, that is voltage across the any element in the network. Symbol is shown in fig.
+
-
a
b
c
d
Vcd
Vab
Fig.1: VCVS
‘k’ is constant (dimensionless)

## Slide 12: BASIC TERMS AND DEFINITIONS
(b) Voltage Controlled Current Source (VCCS):
In this dependent source current of the source iab depends on the voltage Vcd.
iab α Vcd or iab = η Vcd
Where,‘η’ is known as transconductance and its unit is mho.
iab
Fig.2: VCCS
a
b
c
d
Vcd

## Slide 13: BASIC TERMS AND DEFINITIONS
(c) Current Controlled Voltage Source (CCVS):
Voltage of the source Vab depends on the current of branch ‘cd’
Vab α icd or Vab = r icd
Where ‘r’ is the constant, has the unit resistance (i.e Ω )
Vab
Fig.3: CCVS
a
b
c
d
icd
+
-

## Slide 14: BASIC TERMS AND DEFINITIONS
(d) Current Controlled Current Source (CCCS):
Current of the dependent source, depends on the current of branch cd.
iab iab or, iab = β iab
where ‘β’ = is dimensionless constant.
α
Fig.4: CCCS
a
b
c
d
icd
iab

## Slide 15: BASIC TERMS AND DEFINITIONS
Passive Elements: Passive elements are consumers of electrical energy. There are three passive elements in AC circuits.
Resistance: Resistance is the property of material due to which it opposes the flow of current through it. Its unit is ohm (Ω) and symbol is ‘R’.
According to Ohm’s law v = i R
v-i characteristics is shown in fig.
v
i
0
Fig.5: v-i characteristic
R

## Slide 16: BASIC TERMS AND DEFINITIONS
Inductance: Inductance is the property of material due to which it opposes any change in current passing through it. Its unit is Henery (H) and symbol is ‘L’.
Voltage across inductor and current through inductor is given by

## Slide 17: BASIC TERMS AND DEFINITIONS
Capacitance: Capacitance is the property of element due to which it opposes any change in voltage across it. Its unit is Farad (F) and symbol is ‘C’.
Voltage across capacitor and current through capacitor is given by

## Slide 18: BASIC TERMS AND DEFINITIONS
 | Resistance | Inductance | Capacitance
Symbol |  |  | 
Unit | Ohm (Ω) | Henery (H) | Farad (F)
Voltage across |  |  | 
Current through |  |  | 
R
L
C

## Slide 19
THANK YOU
shasansaeed@yolasite.com
hasansaeed872726549.wordpress.com
saeed.moodlecloud.com
syedhasansaeed.gnomio.com

## Slide 20
shasansaeed@yolasite.com
hasansaeed872726549.wordpress.com
saeed.moodlecloud.com
syedhasansaeed.gnomio.com